|||||||||||||||||||||||||
                                            |||||||||||||||||||||||||
                                            |||||||||||||||||||||||||
                                            |||||||||||||||||||||||||

                                                  ASM7 ASSEMBLER

                                                  USER'S MANUAL


                                            |||||||||||||||||||||||||
                                            |||||||||||||||||||||||||
                  Copyright 1988            |||||||||||||||||||||||||
                 Texas Instruments          |||||||||||||||||||||||||
                All rights reserved.        |||||||||||||||||||||||||
                                            |||||||||||||||||||||||||
         The information and/or drawings    |||||||||||||||||||||||||
         set forth in this document  and    |||||||||||||||||||||||||
         all rights in and to inventions    |||||||||||||||||||||||||
         disclosed  herein  and  patents    |||||||||||||||||||||||||
         which might be granted  thereon    |||||||||||||||||||||||||
         disclosing   or  employing  the    |||||||||||||||||||||||||
         materials, methods, techniques,    |||||||||||||||||||||||||
         or  apparatus described  herein    |||||||||||||||||||||||||
         are the  exclusive  property of    |||||||||||||||||||||||||
         Texas Instruments.                 |||||||||||||||||||||||||
                                            |||||||||||||||||||||||||
         No disclosure of information or    |||||||||||||||||||||||||
         drawings shall  be made to  any    |||||||||||||||||||||||||
         other  person  or  organization    |||||||||||||||||||||||||
         without  the prior  consent  of    |||||||||||||||||||||||||
         Texas Instruments.                 |||||||||||||||||||||||||
                                            |||||||||||||||||||||||||
         Texas Instruments Incorporated     |||||||||||||||||||||||||
         Consumer Products Division         |||||||||||||||||||||||||
         P.O. Box 650311  MS 3920           |||||||||||||||||||||||||
         Dallas, TX 75265                   |||||||||||||||||||||||||
                                            |||||||||||||||||||||||||

                                                 TEXAS INSTRUMENTS
                                                    INCORPORATED

                                            |||||||||||||||||||||||||
                                            |||||||||||||||||||||||||
         Document: ASM7 V4.0                |||||||||||||||||||||||||
         Date: 19 SEP 88                    |||||||||||||||||||||||||
                                            |||||||||||||||||||||||||

                                        

                                                          TABLE of CONTENTS






                               TABLE of CONTENTS

          Paragraph                    Title                           Page




                  SECTION 1 Introduction                               1-1

          1.1     Revision . . . . . . . . . . . . . . . . . . . . . . 1-1
          1.2     Overview . . . . . . . . . . . . . . . . . . . . . . 1-1


                  SECTION 2 Running ASM7                               2-1

          2.1     Command Line Options . . . . . . . . . . . . . . . . 2-1
          2.1.1     B  . . . . . . . . . . . . . . . . . . . . . . . . 2-1
          2.1.2     D  . . . . . . . . . . . . . . . . . . . . . . . . 2-1
          2.1.3     F  . . . . . . . . . . . . . . . . . . . . . . . . 2-2
          2.1.4     L  . . . . . . . . . . . . . . . . . . . . . . . . 2-2
          2.1.5     N  . . . . . . . . . . . . . . . . . . . . . . . . 2-2
          2.1.6     O  . . . . . . . . . . . . . . . . . . . . . . . . 2-2
          2.1.7     R  . . . . . . . . . . . . . . . . . . . . . . . . 2-2
          2.1.8     T  . . . . . . . . . . . . . . . . . . . . . . . . 2-2
          2.1.9     X  . . . . . . . . . . . . . . . . . . . . . . . . 2-2
          2.1.10    W  . . . . . . . . . . . . . . . . . . . . . . . . 2-3
          2.2     Source File Format . . . . . . . . . . . . . . . . . 2-3
          2.2.1     Constant Bases . . . . . . . . . . . . . . . . . . 2-3
          2.2.2     Expressions  . . . . . . . . . . . . . . . . . . . 2-3
          2.3     Object File Format . . . . . . . . . . . . . . . . . 2-3
          2.4     Listing File Format  . . . . . . . . . . . . . . . . 2-4


                  SECTION 3 ASM7 Directives                            3-1

          3.1     Location Counter Directives  . . . . . . . . . . . . 3-1
          3.1.1     AORG . . . . . . . . . . . . . . . . . . . . . . . 3-1
          3.1.1.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-1
          3.1.1.2     Description  . . . . . . . . . . . . . . . . . . 3-1
          3.1.2     BES  . . . . . . . . . . . . . . . . . . . . . . . 3-1
          3.1.2.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-1
          3.1.2.2     Description  . . . . . . . . . . . . . . . . . . 3-2
          3.1.3     BSS  . . . . . . . . . . . . . . . . . . . . . . . 3-2
          3.1.3.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-2
          3.1.3.2     Description  . . . . . . . . . . . . . . . . . . 3-2
          3.1.4     DORG . . . . . . . . . . . . . . . . . . . . . . . 3-2
          3.1.4.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-2
          3.1.4.2     Description  . . . . . . . . . . . . . . . . . . 3-3

                                        i




                                                          TABLE of CONTENTS



          3.1.5     EVEN . . . . . . . . . . . . . . . . . . . . . . . 3-3
          3.1.5.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-3
          3.1.5.2     Description  . . . . . . . . . . . . . . . . . . 3-3
          3.1.6     RORG . . . . . . . . . . . . . . . . . . . . . . . 3-3
          3.1.6.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-3
          3.1.6.2     Description  . . . . . . . . . . . . . . . . . . 3-3
          3.2     Assembler Output Directives  . . . . . . . . . . . . 3-4
          3.2.1     IDT  . . . . . . . . . . . . . . . . . . . . . . . 3-4
          3.2.1.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-4
          3.2.1.2     Description  . . . . . . . . . . . . . . . . . . 3-4
          3.2.2     LIST . . . . . . . . . . . . . . . . . . . . . . . 3-4
          3.2.2.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-4
          3.2.2.2     Description  . . . . . . . . . . . . . . . . . . 3-4
          3.2.3     OPTION . . . . . . . . . . . . . . . . . . . . . . 3-5
          3.2.3.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-5
          3.2.3.2     Description  . . . . . . . . . . . . . . . . . . 3-5
          3.2.3.3     B  . . . . . . . . . . . . . . . . . . . . . . . 3-5
          3.2.3.4     D  . . . . . . . . . . . . . . . . . . . . . . . 3-5
          3.2.3.5     F  . . . . . . . . . . . . . . . . . . . . . . . 3-5
          3.2.3.6     R  . . . . . . . . . . . . . . . . . . . . . . . 3-5
          3.2.3.7     T  . . . . . . . . . . . . . . . . . . . . . . . 3-5
          3.2.3.8     X  . . . . . . . . . . . . . . . . . . . . . . . 3-6
          3.2.3.9     W  . . . . . . . . . . . . . . . . . . . . . . . 3-6
          3.2.4     PAGE . . . . . . . . . . . . . . . . . . . . . . . 3-6
          3.2.4.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-6
          3.2.4.2     Description  . . . . . . . . . . . . . . . . . . 3-6
          3.2.5     TITL . . . . . . . . . . . . . . . . . . . . . . . 3-6
          3.2.5.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-6
          3.2.5.2     Description  . . . . . . . . . . . . . . . . . . 3-7
          3.2.6     UNL  . . . . . . . . . . . . . . . . . . . . . . . 3-7
          3.2.6.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-7
          3.2.6.2     Description  . . . . . . . . . . . . . . . . . . 3-7
          3.3     Constant Initialization Directives . . . . . . . . . 3-7
          3.3.1     BYTE . . . . . . . . . . . . . . . . . . . . . . . 3-7
          3.3.1.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-7
          3.3.1.2     Description  . . . . . . . . . . . . . . . . . . 3-8
          3.3.2     DATA . . . . . . . . . . . . . . . . . . . . . . . 3-8
          3.3.2.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-8
          3.3.2.2     Description  . . . . . . . . . . . . . . . . . . 3-8
          3.3.3     EQU  . . . . . . . . . . . . . . . . . . . . . . . 3-8
          3.3.3.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-8
          3.3.3.2     Description  . . . . . . . . . . . . . . . . . . 3-8
          3.3.4     RBYTE  . . . . . . . . . . . . . . . . . . . . . . 3-9
          3.3.4.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-9
          3.3.4.2     Description  . . . . . . . . . . . . . . . . . . 3-9
          3.3.5     RDATA  . . . . . . . . . . . . . . . . . . . . . . 3-9
          3.3.5.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-9
          3.3.5.2     Description  . . . . . . . . . . . . . . . . . . 3-9
          3.3.6     RTEXT  . . . . . . . . . . . . . . . . . . . . . . 3-10
          3.3.6.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-10
          3.3.6.2     Description  . . . . . . . . . . . . . . . . . . 3-10

                                        ii




                                                          TABLE of CONTENTS



          3.3.7     TEXT . . . . . . . . . . . . . . . . . . . . . . . 3-10
          3.3.7.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-10
          3.3.7.2     Description  . . . . . . . . . . . . . . . . . . 3-10
          3.4     Program Linkage Directives . . . . . . . . . . . . . 3-11
          3.4.1     DEF  . . . . . . . . . . . . . . . . . . . . . . . 3-11
          3.4.1.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-11
          3.4.1.2     Description  . . . . . . . . . . . . . . . . . . 3-11
          3.4.2     REF  . . . . . . . . . . . . . . . . . . . . . . . 3-11
          3.4.2.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-11
          3.4.2.2     Description  . . . . . . . . . . . . . . . . . . 3-11
          3.5     Miscellaneous Directives . . . . . . . . . . . . . . 3-12
          3.5.1     COPY . . . . . . . . . . . . . . . . . . . . . . . 3-12
          3.5.1.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-12
          3.5.1.2     Description  . . . . . . . . . . . . . . . . . . 3-12
          3.5.2     END  . . . . . . . . . . . . . . . . . . . . . . . 3-12
          3.5.2.1     Fields . . . . . . . . . . . . . . . . . . . . . 3-12
          3.5.2.2     Description  . . . . . . . . . . . . . . . . . . 3-12


                  SECTION 4 Further Information                        4-1
































                                       iii


          TI-74 ASM7                                           Introduction








          
                                      SECTION 1

                                     Introduction
          



          1.1 Revision

               This   is   revision   4.0   of    this    package,    dated
          September 21, 1988.


          1.2 Overview

               ASM7  is  a  PC-based  assembler  for  the TMS7000 family of
          microcomputers.  ASM7 is full featured, although it does not have
          a macro capability.  This document will cover the  features  that
          the assembler provides, and how to use this assembler.



























          Texas Instruments            1-1




          TI-74 ASM7                                           Running ASM7








          
                                      SECTION 2

                                     Running ASM7
          

          ASM7  is  executed  by  entering  the  'ASM7'  command to the DOS
          prompt.  ASM7 can assemble individual files, or  multiple  files,
          and  can  accept  wildcard  filename specifications (ie. *.ASM to
          assemble all assembly files in one directory).

               Syntax for the command line to ASM7 is:
           
            C:\>ASM7 -options file1,file2,... 
           
          The command line options shown above may or may not be used,  and
          the  filenames  specified  may  be full DOS pathnames (with drive
          specification) or a  filename  in  the  current  directory.   The
          filenames may also contain wildcard specifications.


          2.1 Command Line Options

               ASM7   accepts  command  line  options  of  the  form  "ASM7
          -option_letter...".  The various command line options that may be
          specified are documented in the following paragraphs. Options may
          be specified in either upper or lower case to the assembler.


          2.1.1 B

          The -B option causes BYTE and RBYTE directives to only  list  the
          first  4  bytes  specified.   If not specified, then all BYTE and
          RBYTE directives cause all of their constants to be listed in the
          listing file.


          2.1.2 D

          The -D option causes DATA and RDATA directive to  only  list  the
          first 2 words of data specified, although all data specified will
          be included in the object module file.





          Texas Instruments            2-1




          TI-74 ASM7                                           Running ASM7





          2.1.3 F

          The  -F option is identical to specifying -BDT to disable listing
          of more than 4 bytes of information to the listing file  for  any
          BYTE, RBYTE, DATA, RDATA, TEXT, and RTEXT directive.


          2.1.4 L

          The  -L  option disables listing file generation completely. When
          specified, no listing file will  be  created  from  the  assembly
          process.


          2.1.5 N

          The  -N  option causes line numbers to be included in the listing
          file if one is generated.  The default is to not add line numbers
          to the listing file.


          2.1.6 O

          The -O option disables creation of the output object  module  for
          the  assembled  module.  When specified, no object module will be
          created.  The default is to write the object module.


          2.1.7 R

          The -R option causes a reduced cross  reference  map  of  symbols
          encountered  in  the assembly process to be written.  The default
          is to not write a cross reference map.


          2.1.8 T

          The -T option causes TEXT and RTEXT directives to only generate 4
          bytes of information  in  the  listing  file,  although  all  the
          specified data will be included in the object module.


          2.1.9 X

          The  -X option causes generation of a full cross reference map to
          be included at the end of the listing file.  The  default  is  to
          not write a cross reference map.



          Texas Instruments            2-2




          TI-74 ASM7                                           Running ASM7





          2.1.10 W

          The -W option causes the listing file to not include any assembly
          warnings  that  occurred.   Errors will still be listed after the
          line that they occurred in.


          2.2 Source File Format

               The input source file should use a .ASM extension on the PC.
          All labels start  in  column  one  of  the  file,  with  assembly
          directives  and  mnemonics  preceded by at least one blank space.
          Labels cannot have comments after  them  unless  they  are  first
          followed by an EQU directive.


          2.2.1 Constant Bases

          Constants  in  the  ASM7 assembler are by default, in the decimal
          base.  To  force  a  constant  into  another  base,  one  of  the
          following indicators should precede the constant:
           
                 >    : hexadecimal constant
                 #    : hexadecimal constant
                 ?    : binary constant
                 '    : starts and ends string (text) constant
           


          2.2.2 Expressions

          Expressions  in  ASM7  consist of numeric constants, symbols, and
          operators.  The valid list of operators and their  functions  are
          listed in the following table:
           
                 +    : addition
                 -    : subtraction
                 *    : multiplication
                 /    : integer division
                 %    : integer modulus
                 &    : logical AND function
                 |    : logical OR function
                 ^    : logical XOR function
           


          2.3 Object File Format

               The  object  file  created  will  contain  TI  tagged object

          Texas Instruments            2-3




          TI-74 ASM7                                           Running ASM7



          format.   Refer  to  the  Object  Format  Document  for   further
          information on this format.


          2.4 Listing File Format

               The  listing  file  will contain a single line of output for
          each input line, with the relocatable (or  absolute)  address  of
          that instruction followed by the opcode data for that instruction
          at  the  beginning  of  the  line.   If the line number option is
          specified, then the line will be preceded by the line number  for
          that line.








































          Texas Instruments            2-4




          TI-74 ASM7                                        ASM7 Directives








          
                                      SECTION 3

                                   ASM7 Directives
          

          ASM7  version  4.0  supports  24  directives  that  allow various
          functions to be  performed.   These  directives  are  covered  in
          detail in this section.


          3.1 Location Counter Directives



          3.1.1 AORG

            Syntax: [<label>] AORG <word-expression> [<comment>]
           


          3.1.1.1 Fields

          The  label  is  optional  and if used, is assigned the same value
          that AORG places in the location counter.

               The  word  expression  is  evaluated  and  assigned  to  the
          location counter


          3.1.1.2 Description

          AORG  loads  the  location  counter  with  the   value   of   the
          word-expression.   This  directive causes the object module to be
          an absolute (not relocatable) module.


          3.1.2 BES

            Syntax: [<label>] BES <word-expression> [<comment>]
           


          3.1.2.1 Fields

          The label field is optional and if used, is assigned the value of

          Texas Instruments            3-1




          TI-74 ASM7                                        ASM7 Directives



          the location counter at the end of the reserved block of data.

               The operand field is evaluated, and the value added  to  the
          location counter.


          3.1.2.2 Description

          BES  evaluates  the operand expression and adds this value to the
          location counter.  This directive will  therefore  allocate  byte
          buffers  of  various  sizes,  with the last byte address location
          assigned to the optional label attached to the directive.


          3.1.3 BSS

            Syntax: [<label>] BSS <word_expression> [<comment>]
           


          3.1.3.1 Fields

          The label field is optional and will be assigned the value of the
          location counter at the lowest address of the  block  created  by
          the directive.

               The operand is evaluated and is used by the directive as the
          value to add to the location counter.


          3.1.3.2 Description

          The  BSS  directive  adds  the  expression  value to the location
          counter.  This directive will therefore allocate byte buffers  of
          various  sizes,  with the first byte address location assigned to
          the optional label attached to the directive.


          3.1.4 DORG

            Syntax: [<label>] DORG <expression> [<comment>]
           


          3.1.4.1 Fields

          The label is optional, and if used, is assigned  the  same  value
          that will be placed in the location counter.

               The  operand field contains an expression that can be either
          relocatable or absolute.

          Texas Instruments            3-2




          TI-74 ASM7                                        ASM7 Directives





          3.1.4.2 Description

          DORG loads the location counter with the starting  address  of  a
          dummy block or section.


          3.1.5 EVEN

            Syntax: [<label>] EVEN [<comment>]
           


          3.1.5.1 Fields

          The  label  field  for the EVEN directive is optional and will be
          assigned the value of the location counter after the directive is
          processed if used.


          3.1.5.2 Description

          This directive will force the location counter to the  next  word
          address  boundary.   If the location counter is already at such a
          location, no alteration is performed.


          3.1.6 RORG

            Syntax: [<label>] RORG <expression> [<comment>]
           


          3.1.6.1 Fields

          The label is optional, but if used is  assigned  the  same  value
          that will be assigned to the location counter.

               The  operand  used  must be a relocatable expression and can
          contain only previously defined symbols.


          3.1.6.2 Description

          RORG places the  relocatable  value  of  the  expression  in  the
          location counter.





          Texas Instruments            3-3




          TI-74 ASM7                                        ASM7 Directives





          3.2 Assembler Output Directives



          3.2.1 IDT

            Syntax: [<label>] IDT 'string' [<comment>]
           


          3.2.1.1 Fields

          The  label is optional, but if used is assigned the current value
          of the location counter.

               The operand contains a module name in  the  'string'.   This
          string may be upto 8 characters long.


          3.2.1.2 Description

          IDT  assigns a name to the object module produced by the assembly
          process.  This name can be seen in the link map file produced  by
          TILINK to identify the module easily.


          3.2.2 LIST

            Syntax: [<label>] LIST [<comment>]
           


          3.2.2.1 Fields

          The label is optional, but if used takes the value of the current
          location counter.


          3.2.2.2 Description

          LIST  restores  printing of the listing to the listing file if it
          was cancelled by a previous UNL directive.








          Texas Instruments            3-4




          TI-74 ASM7                                        ASM7 Directives





          3.2.3 OPTION

            Syntax:    OPTION <option-list>
           


          3.2.3.1 Fields

          Labels are not used with the OPTION  directive,  and  no  comment
          should follow an OPTION directive.


          3.2.3.2 Description

          The  OPTION  directive  may  select  several  options relating to
          assembly listing output.  The operand is a list of  keywords  (or
          letters)  separated  by  commas.   Each option selects one of the
          following features (and may be selected by command line option as
          well; see section above.)


          3.2.3.3 B

          The B option limits the listing of BYTE and RBYTE  directives  to
          one line.


          3.2.3.4 D

          The  D  option limits the listing of DATA and RDATA directives to
          one line.


          3.2.3.5 F

          The F option limits  the  listing  of  all  constant  initializer
          directives  (BYTE,  RBYTE,  DATA,  RDATA, TEXT, and RTEXT) to one
          line.  It is the same as using OPTION B,D,T.


          3.2.3.6 R

          The R option causes a reduced cross-reference table of symbols to
          be produced in the listing file.


          3.2.3.7 T

          The T option limits the listing of TEXT and RTEXT  directives  to

          Texas Instruments            3-5




          TI-74 ASM7                                        ASM7 Directives



          one line.


          3.2.3.8 X

          The X option causes a full cross-reference table of symbols to be
          produced in the listing file.


          3.2.3.9 W

          The  W  option  causes the exclusion of warning messages from the
          listing file.


          3.2.4 PAGE

            Syntax: [<label>] PAGE [<comment>]
           


          3.2.4.1 Fields

          The label is optional, but will be  assigned  the  value  of  the
          location counter if present.


          3.2.4.2 Description

          The  PAGE  directive  causes  a page eject in the source listing,
          with listing immediately continued on the next page.


          3.2.5 TITL

            Syntax: [<label>] TITL 'string'
           


          3.2.5.1 Fields

          The label field is optional, but will be assigned  the  value  of
          the current location counter if present.

               The 'string' field contains the assembly title to be used on
          line 2 of each page of the listing file.  Up to 60 characters may
          be specified in the title string.





          Texas Instruments            3-6




          TI-74 ASM7                                        ASM7 Directives





          3.2.5.2 Description

          The  TITL  directive  supplies  a page title for each page of the
          assembly listing, and can occur more than once in a  module  (for
          different  page  titles).   The title will be printed on the next
          page after the TITL directive is encountered.


          3.2.6 UNL

            Syntax: [<label>] UNL  [<comment>]
           


          3.2.6.1 Fields

          The label field is optional and will be assigned the value of the
          location counter if present.


          3.2.6.2 Description

          The UNL directive stops  program  listing  output  until  a  LIST
          directive  is  encountered.  This is useful when assembling files
          with many included COPY files that do not require listing.


          3.3 Constant Initialization Directives



          3.3.1 BYTE

            Syntax: [<label>] BYTE <exp>[,<exp>] [<comment>]
           


          3.3.1.1 Fields

          The label field is  optional,  but  takes  the  current  location
          counter value if present.

               The operand field contains one or more expressions separated
          by commas.  These expressions cannot contain external references.
          The assembler evaluates these expressions and places the value in
          a  byte.   If  truncation  is  required,  the  assembler prints a
          truncation warning and puts the LSB of the value in the byte.



          Texas Instruments            3-7




          TI-74 ASM7                                        ASM7 Directives





          3.3.1.2 Description

          The BYTE directive places one or  more  values  in  one  or  more
          successive bytes of memory.


          3.3.2 DATA

            Syntax: [<label>] DATA <exp>[,<exp>] [<comment>]
           


          3.3.2.1 Fields

          The  label  field  is  optional,  but  takes the current location
          counter value if present.

               The operand field contains one or more expressions separated
          by commas.  These expressions can  contain  external  references.
          The assembler evaluates these expressions and places the value in
          a  word  as  a  16-bit number, most significant byte first (lower
          address).


          3.3.2.2 Description

          The DATA directive places one or more words of  data  in  one  or
          more successive 2-byte words of memory.


          3.3.3 EQU

            Syntax: <label> EQU <expression> [<comment>]
           


          3.3.3.1 Fields

          The  label  field  is required and contains a symbol that will be
          assigned the operand's value.

               The operand is an expression whose value will be assigned to
          the label.  The operand may not  contain  a  REF'd  symbol  or  a
          forward reference.


          3.3.3.2 Description

          The EQU directive assigns a value to a symbol.

          Texas Instruments            3-8




          TI-74 ASM7                                        ASM7 Directives





          3.3.4 RBYTE

            Syntax: [<label>] RBYTE <exp>[,<exp>] [<comment>]
           


          3.3.4.1 Fields

          The  label  is optional and will be assigned the current location
          counter value if present.

               The operand field contains one or more expressions that will
          be evaluated, and their values treated as 8-bit numbers, assigned
          to one or more successive byte locations.


          3.3.4.2 Description

          The RBYTE directive is similar to the BYTE directive except  that
          the 8-bit value is stored in reverse digit fashion.  For example,
          if  the  value  >A6  is  given  as  the  expression  to  the BYTE
          directive, the location will contain >A6.  This same value  given
          the RBYTE directive will contain >6A (nibble reversal).


          3.3.5 RDATA

            Syntax: [<label>] RDATA <exp>[,<exp>] [<comment>]
           


          3.3.5.1 Fields

          The  label  is  optional  but  will  be assigned the value of the
          current location counter if present.

               The operand field contains one or more expressions that will
          be evaluated to a 16-bit number, and  assigned  in  byte-reversed
          order to successive byte locations.


          3.3.5.2 Description

          The RDATA directive is similar to the DATA directive, except that
          instead  of  storing  the data words in the form MSB at the lower
          address, the RDATA directive stores the data word in the form LSB
          at the lower address.



          Texas Instruments            3-9




          TI-74 ASM7                                        ASM7 Directives





          3.3.6 RTEXT

            Syntax: [<label>] RTEXT [-]'string' [<comment>]
           


          3.3.6.1 Fields

          The label is optional and will be assigned the  current  location
          counter value if present.

               The  operand  contains  the  string  data  to  be  stored in
          successive bytes of memory in reverse order (ie. first  character
          of  string stored at highest byte).  If the string is preceded by
          a unary minus, the highest addressed character will have its most
          significant bit set (same as or'ing it with 128).


          3.3.6.2 Description

          The RTEXT directive stores a string in reverse order  in  memory,
          with  the  last  character  of  the  operand  field at the lowest
          address in memory.


          3.3.7 TEXT

            Syntax: [<label>] TEXT [-]'string' [<comment>]
           


          3.3.7.1 Fields

          The label is optional and will be assigned the  current  location
          counter value if present.

               The  operand  contains  the  string  data  to  be  stored in
          successive bytes of memory in the order encountered in the string
          (ie. first character stored  at  the  lowest  address).   If  the
          string  is  preceded  by  a  unary  minus,  the highest addressed
          character will have its most significant bit set (same as  or'ing
          it with 128).


          3.3.7.2 Description

          The  TEXT  directive  stores  a string in normal order in memory,
          with the last character of  the  operand  field  at  the  highest
          address in memory.

          Texas Instruments            3-10




          TI-74 ASM7                                        ASM7 Directives





          3.4 Program Linkage Directives



          3.4.1 DEF

            Syntax: [<label>] DEF <symbol>[,<symbol>] [<comment>]
           


          3.4.1.1 Fields

          The  label  is optional and if present takes the current value of
          the location counter.

               The operand field contains one or more symbols, separated by
          commas, to be defined in the program  being  assembled.   If  the
          symbols are not encountered in the module, the assembler produces
          and undefined symbol error for each symbol.


          3.4.1.2 Description

          DEF  makes  one or more symbols available to other programs.  All
          symbols used in the DEF statement must be  defined  in  the  same
          module.   The  symbols  encountered  in the DEF statement will be
          included in the object module output file.


          3.4.2 REF

            Syntax: [<label>] REF <symbol>[,<symbol>] [<comment>]
           


          3.4.2.1 Fields

          The label field is optional and will be given the  value  of  the
          current location counter.

               The operand field contains one or more symbols, separated by
          commas,  defined  in  other  modules,  that are to be used in the
          current module.


          3.4.2.2 Description

          REF provides access to one  or  more  symbols  defined  in  other
          programs.   An  error occurs at link time if the REF'd symbol has

          Texas Instruments            3-11




          TI-74 ASM7                                        ASM7 Directives



          not been DEF'd in another module.


          3.5 Miscellaneous Directives



          3.5.1 COPY

            Syntax: [<label>] COPY <filename> [<comment>]
           


          3.5.1.1 Fields

          The label is optional and will be given the current value of  the
          location counter if present.

               The  filename in the operand field must correspond to a file
          that exists on the system being  used  to  assemble  the  module.
          Nested copying of files is not allowed with this release of ASM7.


          3.5.1.2 Description

          COPY changes the source input for the assembler to the file named
          in  the  operand  field.   When END-OF-FILE is encountered on the
          COPY file, then input processing resumes with the original source
          input file.


          3.5.2 END

            Syntax: [<label>] END
           


          3.5.2.1 Fields

          The label is optional and is  given  the  value  of  the  current
          location counter if present.


          3.5.2.2 Description

          The END directive indicates to the assembler the end of the input
          source  file.  This directive should be the last source statement
          of the primary assembly file and should never be used in  a  COPY
          file.



          Texas Instruments            3-12




          TI-74 ASM7                                    Further Information








          
                                      SECTION 4

                                 Further Information
          

          For complete information on the TMS7000 assembly language, please
          refer to the TMS7000 Assembly Language Programmer's Guide. (TI PN
          1602127-9701)

               For  information regarding the TMS7000 Series microprocessor
          family,  refer  to  the  TMS7000  Family  Data  Manual.  (TI   PN
          1603481-9701 rev B)

               Either of these documents should be available from the local
          TI Sales Office.































          Texas Instruments            4-1